## Slide 1: EECS 70A: Network Analysis
Lecture 16
Comprehensive review
Announcements:
Final HW due Friday of 10th week
Professor Burke’s office hours this week: Tu 9:30-11:30 (EH 2230) Th 9:30-11 (EG 2232) Th 2-3:30 (EH 2230)
Exam :
  Will cover all of Chs. 1,2,3,4,6, 7.1-7.3, 9 (not delta-Y), 14.1 14.2 14.3 14.5 14.6 14.7
  Not covered: 3.6, 3.8, 4.9, 6.6.
  No calculators. We will give sin, cos, tan tables as shown on last slide of today’s notes..

## Slide 2: Topics covered
KCL, KVL
Nodal analysis
Mesh analysis
Thevenin/Norton theorem
RL, RC circuits (time dependence)
R,L,C circuits
  Phasors
  Impedances
  Transfer function

## Slide 3: Thevenin, Norton Theorems:
a
b
+
-
Rth
+
-
Vth
Equivalent to:
a
b
+
-
RN
IN
Equivalent to:
a
b
+
-
Thevenin:
Calculating Vth: Connect nothing to a-b. Calculate voltage. This is Vth.
Calculating Rth:
  Method 1: Connect terminal a to b (short). Calculate the current from a to b. This is call Ishort circuit.
  Rth=Vth/Ishort circuit.
  Method 2: Find the input resistance looking into terminals a-b after all the independent sources have been turned off. (Voltage sources become shorts, current sources become opens.) Trick (if dependent sources present): Apply a 1 A current source to terminals a-b, find Vab
  Rth = Vab/1A.
Linear two-terminal circuit
Norton:
Calculating RN: RN=Rth
Calculating IN:
  IN=Vth/Rth

## Slide 4
Find V(t), q(t), i(t)
C
+
-
V
R
RC circuit

## Slide 5: LR circuit
Find V(t), i(t)
R
+
-
V
L1

## Slide 6: Comprehensive Example
1 kW
a
b
+
-
+
-
3 V
This circuit is connected to a capacitor of value 1 mF. The switch is in the closed position. After a long time, what are all the voltages and currents in this circuit?
Next, the switch is opened. What are all the voltages and currents in this circuit as a function of time after the switch is opened?
This circuit is now connected to a resistor R0. What is the power dissipated in R0?
If you were to pick a value of R0 to absorb as much power as possible, what would it be?
Exercise: Do the same as A,B with an inductor instead.
3 kW
2 kW
4kW

## Slide 7: Comprehensive Example
1 kW
a
b
+
-
+
-
3 V
3 kW
2 kW
4kW

## Slide 8: Comprehensive Example
1 kW
a
b
+
-
+
-
3 V
3 kW
2 kW
4kW

## Slide 9: Conversion procedures
i(t)
V
I =
I
v(t)
V
i(t)
I
v(t)
V
V =
I
For the exam, you should know how to carry out these procedures.

## Slide 10: Circuits
+
-
V
L
C
+
-
V
R
V = I R
V=I/jwC
V=jwL I
“Impedance”
Z = R
Z=1/jwC
Z = jwL
KCL, KVL hold for relationship between V, I.

## Slide 11: Series/Parallel Impedances
Z eq= Z 1 +Z 2 +Z 3
Z1
Z2
Z3
=
Zeq
Z1
Z2
Z3
=
Zeq
Z eq-1 = Z 1-1 +Z 2-1 +Z 3-1

## Slide 12: Conversion procedures
i(t)
I
v(t)
V = I Zeq
Zeq
i(t)
+
-
v(t)
Given i(t) find v(t):
v(t)
V
i(t)
I = V/ Zeq
Given v(t) find i(t):
For the exam, you should know how to carry out these procedures.

## Slide 13: “Transfer Function”
Linear network
Input
Output
H(w) = Vout/Vin

## Slide 14: Phasor Example 1
10 kW
3 cos(w t+30deg)
Find v(t).
2 mF
+
-
V
1 kW
25 mH

## Slide 15: Phasor Example 2
3 kW
4cos(w t+45deg)
Find v(t).
+
-
V
1 kW
1 mH
5kW

## Slide 16: Example Transfer function
Calculate H(w) for this circuit. Sketch the magnitude of H(w) vs. w.
Vout
+
-
Vin
+
-
R2
R1
L1
L2

## Slide 17: Symbol library
+
-
+
-
2
+
-
i7
2 W
3 A
+
-
3 i1
2 i1
+
-
3 V
i7
i7
C
i
+
-
V

## Slide 18: Exam cheat sheet
This will be provided with the exam.