## Slide 1: EECS 70A: Network Analysis
June 5, 2014
Comprehensive review

## Slide 2: Topics covered
KCL, KVL
Nodal analysis
Mesh analysis
Thevenin/Norton theorem
RL, RC circuits (time dependence)
R,L,C circuits
  Phasors
  Impedances
  Transfer function/Bode
  Power

## Slide 3: Nodal Analysis(Review)
Based on KCL, use node voltages as circuits variables.
Define a reference node.
Label remaining nodes. (n-1 nodes)
Apply KCL + ohm to all nodes and supernodes (e.g. V1, V2, V3, …)
    Express all i’s in terms of v’s
Apply KVL to the voltage source
  If one end of voltage source connected to ground, don’t need to
Solve the n-1 simultaneous equations, to find V’s
Use Ohm’s law to find the currents.

## Slide 4: Mesh analysis summary
Assign mesh currents i1, i2, … in
Apply KVL + Ohm’s law to each mesh
Supermesh (if there is a current source present):
CASE 1: current source only in one mesh.
  Already have the current for that mesh => no need to write KVL for that mesh
CASE 2: current source exits between two meshes. => create a supermesh
  Apply KVL to the supermesh
  Apply KCL to a node in the branch where two meshes intersect
Solve the equations for i1 ,i2 ,…in (e.g. using Kramer’s rule)
Then solve for voltages using Ohm’s law
Based on KVL, use mesh currents as circuit variables.

## Slide 5: Thevenin, Norton Theorems:
a
b
+
-
Rth
+
-
Vth
Equivalent to:
a
b
+
-
RN
IN
Equivalent to:
a
b
+
-
Thevenin:
Calculating Vth: Connect nothing to a-b. Calculate voltage. This is Vth.
Calculating Rth:
  Method 1: Connect terminal a to b (short). Calculate the current from a to b. This is call Ishort circuit.
  Rth=Vth/Ishort circuit.
  Method 2: Find the input resistance looking into terminals a-b after all the independent sources have been turned off. (Voltage sources become shorts, current sources become opens.) Trick (if dependent sources present): Apply a 1 A current source to terminals a-b, find Vab
  Rth = Vab/1A.
Linear two-terminal circuit
Norton:
Calculating RN: RN=Rth
Calculating IN:
  IN=Vth/Rth

## Slide 6: Conversion procedures
i(t)
V
I =
I
v(t)
V
i(t)
I
v(t)
V
V =
I
For the exam, you should know how to carry out these procedures.

## Slide 7: Circuits
+
-
V
L
C
+
-
V
R
V = I R
V=I/jwC
V=jwL I
“Impedance”
Z = R
Z=1/jwC
Z = jwL
KCL, KVL hold for relationship between V, I.

## Slide 8: Series/Parallel Impedances
Z eq= Z 1 +Z 2 +Z 3
Z1
Z2
Z3
=
Zeq
Z1
Z2
Z3
=
Zeq
Z eq-1 = Z 1-1 +Z 2-1 +Z 3-1

## Slide 9: Conversion procedures
i(t)
I
v(t)
V = I Zeq
Zeq
i(t)
+
-
v(t)
Given i(t) find v(t):
v(t)
V
i(t)
I = V/ Zeq
Given v(t) find i(t):
For the exam, you should know how to carry out these procedures.

## Slide 10: “Transfer Function”
Linear network
Input
Output
H(w) = Vout/Vin

## Slide 11: Example Transfer function
Calculate H(w) for this circuit. Sketch the magnitude of H(w) vs. w.
Vout
+
-
Vin
+
-
R2
R1
L1
L2

## Slide 12: Bode example
Find Vout(t) given:
Vin(t)= 1 mV cos ( 2*pi*1kHz*t)

## Slide 13: Comprehensive Example
1 kW
+
-
3 kW
2 mF
25 mH
3 cos(w t+30deg)
Solve all currents, voltages using Nodal. Do again using mesh.

## Slide 14: Comprehensive Example
1 kW
+
-
3 kW
2 mF
25 mH
3 cos(w t+30deg)
Solve all currents, voltages using Nodal. Do again using mesh.

## Slide 16: Phasor Example 2
3 W
4cos(w t+45deg)
Find Thev Eq Circ + max pwr txfr load impedance.
1 W
1 mH
5W
Vout
+
-

## Slide 17: Phasor Example 1
10 kW
3 cos(w t+30deg)
Find v(t).
2 mF
+
-
V
1 kW
25 mH

## Slide 18: Symbol library
+
-
+
-
2
+
-
i7
2 W
3 A
+
-
3 i1
2 i1
+
-
3 V
i7
i7
C
i
+
-
V

## Slide 19: Exam cheat sheet
This will be provided with the exam.