## Slide 1: EECS 70A: Network Analysis
Lecture 1

## Slide 2
Northeast Blackout 2003
What:
256 power plants down
55 million people affected
How did this happen?

## Slide 3: Power Networks
How much power used?
How do we quantify power?
What if someone turns on one light?

## Slide 4: Digital circuits
How do we understand what every transistor is doing?
There are hundreds of millions…

## Slide 5: Simplifications
Leon Charles Thevenin
1857–1926
Edward Lawry Norton
1898–1983
Ultimate problem solvers: Take a complex system, break it into its component parts:
Network analysis

## Slide 6: Current
i
Current is flow of charge.
In a wire, charges are free electrons.
Charge of an electron:
e = -1.6 x 10-19 Coulomb [C]
i = dq/dt
Amperes [A] = Coulombs/second [C]/[s]

## Slide 7: Examples
1 electron per second flows past a plane.
What is the current? (instructor)
10 A of current flows.
How many electrons per second flow past a plane? (students)

## Slide 8: Demo circuit: Current source
i
i
Our first circuit element: Current source

## Slide 9: Voltage
Physically, how do we get electrons to move? Apply a force.
E electric field: Volts/meter [V/m]
V voltage (aka potential difference): Volts [V]
CIRCUIT
a
b
Vab ≠ 0 => electrons pushed a to b, causing current to flow

## Slide 10: Voltage source
Our next circuit element: Voltage source
Makes Vab constant, regardless of how much current flows through it.

## Slide 11: Dependent sources
Value of voltage is determined by something somewhere else in circuit.
Value of current is determined by something somewhere else in circuit.

## Slide 12: Circuit elements
Independent
sources
Dependent
sources
A dependent source is an active element in which the source quantity is controlled by another voltage or current.
They have four different types: VCVS, CCVS, VCCS, CCCS. Keep in minds the signs of dependent sources.

## Slide 13: Power
a
b
I
I x Vab = power
Watts [W] = Volt Amp [V-A]
Note: MKSA unit system: Meters Kilogram Second Amp

## Slide 14: Examples
a
b
I=1A
Vab = 100 Volts
P = ?
a
b
I=5A
P = 10 W
Vab = ?
(instructor)
(students)

## Slide 15: Sign convention
a
b
Iab
Vab positive => Va > Vb
Iab positive => current flows from a to b
+
-
Vab negative => Va < Vb
Iab negative => current flows from b to a
Define convention first, then solve problem.
P > 0 means power flowing into element (e.g. resistor)
P < 0 means power flowing out of element (e.g. battery)

## Slide 16: Example
V = 120 V @ socket (assume DC).
Cost of electricity is 10 cents/kW-h
Day nothing, night 10 light bulbs on (100 W bulbs) for 1 hr.
What is monthly electric bill?
(instructor)

## Slide 17: Topology
i1
i2
i3
i1=i2+i3
Like water in a river…
V
V
V
Voltage same everywhere….
Concept of a node

## Slide 18: Example
1
I1=2 A
10 V
+
-
2
I3
I3 = ?
Velement 1 = ?
Velement 2 = ?
Power supplied by source =?
(instructor)
I2=3 A

## Slide 19: Example
1
I1
120 V
+
-
2
I2
Itotal
Three light bulbs (100 W each) on 1 hour/night. 120 V @ socket.
What is I per bulb?
What is Itotal from supply?
What is bill?
3
I3
(student)

## Slide 20: Power failure example
1
I1
120 V
+
-
2
I2
Itotal
Generator will fail of power required > 1 MW
How many light bulbs need to be turned on to damage the generator?
3
I3
N
IN