## Slide 1: Example
1
I1
120 V
+
-
2
I2
Itotal
Three light bulbs (100 W each) on 1 hour/night. 120 V @ socket.
What is I per bulb?
What is Itotal from supply?
What is bill?
3
I3
(student)

## Slide 2: EECS 70A: Network Analysis
Lecture 2
Announcements:
HW
Quiz

## Slide 3: Review & agenda
Last lecture:
Current
Voltage
Power
Today:
Examples
  Power (sink/source)
  Current (postive/negative)
  Dependent sources
Resistors
  Series
  Parallel

## Slide 4: MKSA units-cheat sheet
Quantity | Name | Symbol | Expression in terms of other units | Expression in terms of MKSA base units
Frequency | Hertz | Hz |  | s-1
Force | Newton | N |  | m-kg/s2
Pressure | Pascal | Pa | N/m2 | kg/m-s2
Energy | Joule | J | N-m | kg-m2/s2
Power | Watt | W | J/s | kg-m2/s3
Charge | Coulomb | C |  | A-s
Voltage | Volt | V | W/A | kg-m2/A-s3
Capacitance | Farad | F | C/V | A2-s4/kg-m2
Resistance | Ohm | W | V/A | kg-m2/A2-s3
Conductance | Siemens | S | A/V | A2-s3/kg-m2
Inductance | Henry | H |  | kg-m2/A2-s2

## Slide 5: Power: Source vs. sink
a
b
Iab
P = Iab x Vab
P > 0
“sink”: power delivered to element
P < 0
“source”: power supplied by element
+
-

## Slide 7: “source”
10 V
+
-
I=5 A

## Slide 8: “source”
10 V
+
-
I=5 A
Draw or think of as:
a
b
+
-
I=5 A
Vab = 10 V
Iab = - 5 A
a
b
+
-
I=5 A
Vab = 10 V
Iab = - 5 A
Same as:
P = Iab x Vab
= (- 5 A) x (10 V)
= -50 W

## Slide 9: Practice problems
Find the power absorbed or supplied by the element (instructor).
a
b
+
-
I=5 A
Vab = - 3 V
Find the power absorbed or supplied by the element (instructor).
a
b
+
-
I=10 A
Vab = + 5 V

## Slide 10: Practice problems
Find the power absorbed or supplied by the element (student).
a
b
+
-
I=10 A
Vab = + 3 V
Find the power absorbed or supplied by the element (student).
a
b
+
-
I=3 A
Vab = - 2 V

## Slide 11: Topology
i1
i2
i3
i1=i2+i3
Like water in a river…
V
V
V
Voltage same everywhere….
Concept of a node

## Slide 13: Example
1
I1=2 A
10 V
+
-
2
I3
I3 = ?
Velement 1 = ?
Velement 2 = ?
Power supplied by source =?
(instructor)
I2=3 A

## Slide 14: Example problem: Current (positive/negative)
i1= + 2A
i3
i2
5 A
Find the i2, i3 (instructor).
i1
i2
i3
i1=i2+i3
Like water in a river…
Recall:

## Slide 15: Dependent sources
VCVS: Voltage controlled voltage source
CCVS: Current controlled voltage source
VCCS: Voltage controlled current source
CCCS: Current controlled current source

## Slide 16: Voltage controlled voltage source (VCVS)
+
-
1
+
-
2
a
b
c
5 V
5 Vab
Find the voltage drop across element 2 (instructor).

## Slide 28: Voltage controlled current source (VCCS)
1
+
-
2
a
b
5 V
Find the current through element 2 (student).
2 Vab

## Slide 29: Example problem.
Find the Vbc (instructor).
+
-
a
b
c
10 Vbc
2 A
3 A
5 A

## Slide 31: Example
a
b
speaker
speaker
+
-
10 x Vab
or
100 x Vab
or
1,000 x Vab
“amplifier”

## Slide 32: Questions?

## Slide 33: Resistors
a
b
+
-
Iab
Vab = Iab x R
Resistance units: Ohms [W]
Example circuit:
(Voltage source in series with resistor.)
R

## Slide 35: Example problem: Resistors in parallel.
10 V
i3
Solve for all the currents and voltages in this circuit. (instructor).
+
-
i2
i1
i0
R0=2 W
R0=2 W
R0=2 W
a
b

## Slide 36: Example problem: Resistors in parallel.
10 V
i2
Solve for all the currents and voltages in this circuit. (students).
+
-
i1
i3
R0
R0=2 W
2R0
a) Find i1
b) Find i2
c) Find i3
d) Find Req

## Slide 37: Generalize: N resistors in parallel.
i3
Solve for Req. (instructor).
+
-
i2
i1
i0
R1
R2
R3
a
b
Req=?
V0

## Slide 38: Example problem:
Solve for Req. (sudents).
4 W
a
b
Req=?
2 W
4 W

## Slide 39: Important practical example:
Solve for Req. (instructor).
1 M W
a
b
Req=?
1 W

## Slide 40: Questions?

## Slide 45: Voltage addition in circuits
1
2
a
b
c
Vac=Vab+Vbc

## Slide 47: 2 resistors in series
R2
R1
a
b
c
i1
i2

## Slide 48: Generalize: N resistors in series
R2
R1
R3
RN
=
Req

## Slide 49: Example problems
a
b
1 kW
500 W
Solve for Req. (instructor).
a
b
1 W
1 MW
Solve for Req. (students).

## Slide 50: Questions?

## Slide 51: Example problems
R1
R2
R4
R3
Solve for Req. (instructor).

## Slide 52: Example problems
R1
R2
R3
R4
Solve for Req. (students).

## Slide 53: Example problems
R3
R4
R2
R6
R5
R1
Solve for Req. (instructor).

## Slide 54: Example problems

## Slide 55: Voltage divider
R2
R1
+
-
Vin
Vout
Why important?
Concept of source/load. (Thevenin…)

## Slide 56: Source/load concept

## Slide 57: Symbol library
a
b
+
-
a
b
Iab
+
-
a
b
+
-
I=5 A

## Slide 58: Symbol library
+
-
+
-
2